## Slide 1: R E S E T Roadmap for European research on Smartcard Technologies
RESET Seminar - 3 April 2003
Brussels
FROM SMART CARD TO TRUSTED PERSONAL DEVICE
Challenges for future technology

## Slide 2: R E S E T Roadmap for European research on Smartcard Technologies
Pieter Hartel (University Twente)
Eduard de Jong (Sun Microsystems)
Challenges for future technology
Integration in networked systems and environments

## Slide 3: Over view
What is a trusted device
How can it be integrated in a networked society

## Slide 4: What is not a trusted device?
A slave to the reader
a flat PC

## Slide 5: What is a trusted device?
Requirements
  Guards your privacy
  Does what you want it to do
  Refuses to do what others want
Challenges
  how to realise all three requirements
  How to integrate the device into a networked society

## Slide 6: The device guards your privacy
Offers a high level of tamper resistance
  Multiple levels of defences
  Small trusted computing base within the card
Discloses nothing when communicating
  Zero knowledge protocols
  Observers

## Slide 7: The device does what you want it to do
Certifiable
  Tool scalability
  Expense
Interacts directly with the user
  Keyboard & display
  Biometrics

## Slide 8: The device refuses to do what others want
Embeded in a larger trusted device
  Finread
  Puts the problem somewhere else
Prevents pin re-use

## Slide 9: How to realise all three
Can we
  Prove that all three are satisfied?
  Measure to what extent they are satisfied?
Is there an underlying theory?

## Slide 10: AmI component that must be integrated into society
Communication speed & protocols
Self powered
Form factor
Backwards compatibility
New application areas
Not to throw the baby out with the bath water...

## Slide 11: R E S E T Roadmap for European research on Smartcard Technologies
RESET Seminar
3 April 2003
Brussels
FROM SMART CARD TO TRUSTED PERSONAL DEVICE

## Slide 12: R E S E T Roadmap for European research on Smartcard Technologies
Dr. Ulrich BÜKER
ORGA Systems GmbH
RESET Workgroup Leader
Challenges for future technology
Systems Management

## Slide 13: Challenges Systems Management
on-card
Operating Systems
Development Tools
System Integration
Card accepting devices
Card and Device Management
off-card

## Slide 14: Challenges Operating Systems
Standard operating system features
  multi-application, multi-threading
  high-level memory management
Smart Card specific OS features
  resource control management
    deadlock prevention / detection
    optimised resource usage
Support of new communication models
  peer-to-peer
  TCP/IPv6

## Slide 15: Challenges Operating Systems
Main Barriers
  variety of smart card hardware
    hinders the development of more sophisticated operating systems and programming languages
    enormous porting costs
  limited resources on smart card
    difficult adaption of state of the art IT techniques

## Slide 16: Challenges Development Tools
Expressive programming languages
  integrating features of general-purpose languages
  support of smart card specific idioms
  domain-specific languages
Modelling and Specification
  considered in the design of programming languages
  program proofs

## Slide 17: Challenges Development Tools
Main challenges
  improve security
  improve certification process
Formal Methods on different levels
  formal modelling
  formal verification
  program verification

## Slide 18: Challenges System Integration
Main challenges
  integration of smart cards into information systems
    adaptation of software engineering results : middleware, integration tools
  management of smart cards and their content
    smart cards as application servers
    fundamental approach for defining the model

## Slide 19: Challenges System Integration
Advanced smart card programmability and usage
  on-card and off-card frameworks
    extensible
    scalable
  dynamic management of card framework services
  middleware technologies
    scenario and application independent

## Slide 20: Challenges Card Accepting Devices
Physical properties
  incorporation into everyday objects
    e.g. watch, ring
  secure CADs
    prevention of Trojan horses when entering data
      e.g. PIN, biometrics
Data transmission
  wireless, secure channel between CAD and network
  high speed protocols to be supported

## Slide 21: Challenges Card / Device Management
Standard architectures of CADs
  STIP, FinRead, GlobalPlatform
  common test suites needed
  security certification procedures
Shared infrastructures between card and terminal
  less expensive
  increased trust
  management of different user credentials

## Slide 22: R E S E T Roadmap for European research on Smartcard Technologies
RESET Seminar
3 April 2003
Brussels
FROM SMART CARD TO TRUSTED PERSONAL DEVICE

## Slide 23: R E S E T Roadmap for European research on Smartcard Technologies
Jean-Paul THOMASSON
STMicroelectronics
Challenges for Secure System On Chip & System On Card

## Slide 24: The Age of TOTAL ACCESS
Giving customers what they want in an “Anytime, Anywhere World”
The ages of “Reach and Push” are marketing legacy
Direct dialogue between the customer and the producer.
Five “Laws” approach.
Smart Card: the perfect enabling technology for the Age of Total Access

## Slide 25: Five Laws (1)
Moore’s Law: the Number of Transistors on a chip doubles every 18 to 24 months.
Metcalfe’s Law: the value of the network increases by the square of the number of users.
Gilder’s Law: the communications bandwidth is growing faster than computing power by doubling every year.It will continue to do so for the next twenty-five years.

## Slide 26: Five Laws (2)
Law of Storage: Infinite storage for an Infinite Amount of Information. For the network revolution to progress, storage and memory performance with corresponding decreases in cost must expand at a rate faster than in Moore’s law.
Software Law: there is No Law. Software is hard, it’s more about framing human activity than about technology.

## Slide 27: The Challenge for Smart Card
Rich
Challenge
Sec. SoC
Reach
Volume
Features

## Slide 28: System On a Chip definition in year 2005
“On a single chip co-location of sense, compute,control,store,communicate and actuate capabilities” J. Borel Smart card IC’s are Secure System On Chip

## Slide 29: System On a Chip definition
LCD’s
Sensors
Antennas
Keyboards
Loudsp.
Power
Management
Memories
µP, DSP
Data
Acquisition
Power
Actuators
Information
Processing
(Super-integration)
Multifunction
Peripheral
Line

## Slide 30: Developer requirements
Developers require high density re-programmable NVM
  High end products today have more than 300Kbyte ROM
  ROM masking painful as:
      Cycle time for prototypes = weeks
      “Bug free” code more difficult with large system
      Advanced systems specifications keep moving
  Capability to download code “over the air”
      Possibility to add new functions (longer card life)
      Improved security (updated protections - safer card life)
  Limited cards inventory
      Few types inventory may cover product broad range
      Programs may be downloaded at test or personalisation
  Performances (speed & low power)

## Slide 31: The perfect NVM answer
SRAM speed - DRAM / FLASH density
Infinite retention – No fatigue
Enough but not too much write energy
  Resistant to various perturbation
  Very low power
No information “leakage”
Simple standard CMOS process cost
Simply does not exist !

## Slide 32: Economical side
SMARTCARD MARKET
  Around 1% of semiconductor market
    Cannot justify specific technology development
    Today large density EEPROM are only used in smartcard
  Consumer type market
    Medium-High volume / very low price
    Industrial & reliable solution
Must use a standard & proven NVM process (volume on commodity products)

## Slide 33: Technology side
Speed: FRAM, MRAM, PCM
Density: FLASH, PCM
Retention: EEPROM & FLASH (not yet proven for others)
Cycling: MRAM, PCM
Overhead: FRAM, MRAM
Power: FRAM (destructive read!)
Scalability: FLASH, PCM
Volume production: EEPROM & FLASH
Process cost: no HV in MRAM/FRAM/PCM but material?
Process compatibility:
  FRAM, MRAM, PCM can be added on standard CMOS
  No need for special high voltage devices

## Slide 34: Enhancing performances
MOS Performance and leakage for low power.
Production of Non-classical CMOS
CMOS Integration of new Memory material.
Starting material beyond 300mm
Mask-making & cost
Coordinated design tools & simulators to address chip and assembly issues.

## Slide 35: Design difficult challenges (HW& SW)
Productivity to avoid exponentially increasing design costs. Re-use.
Power management.
Interference: resource-efficient communication and synchronisation.
System-level integration of heterogeneous technologies
Error tolerance relaxing for cost reduction ?
Development of SOC test methodologies including for Security.(DFT DF Secure T)

## Slide 36: Conclusion
We need strong and consistent R&D programs in technology challenging domains:
  architecture design and simulation
  semiconductor & heterogeneous technologies integration
  embedded software
  cost effective manufacturing
  security development and testing
To bring to the market the necessary Innovations that will restore the Industry Growth and Profitability.

## Slide 37: R E S E T Roadmap for European research on Smartcard Technologies
RESET Seminar
3 April 2003
Brussels
FROM SMART CARD TO TRUSTED PERSONAL DEVICE

## Slide 38: R E S E T Roadmap for European research on Smartcard Technologies
Challenges for future technology
Smart Card Security
Dr. Albert MÖDL
Giesecke & Devrient GmbH

## Slide 39: Challenges Smart Card Security
SECURE semiconductors for smart cards
Enhanced subsystem security
Card OS / software with high security level
Ubiquitous security through
communication and networks protocols
Reliable and secure interplay with card
accepting devices
Enhanced security for the overall system

## Slide 40: Challenges: Secure Semiconductors
Resistance to invasive and non-invasive attacks
  elaborate chip-architecture and design
    glue logic (randomization of the layout)
    bus scrambling (data are scrambled)
  constant-current mode
Tamper resistance
  tamper-evident and removal-resistant coatings
  tamper detection mechanisms (sensors & actors)
    tamper response and zeroization circuitry

## Slide 41: Challenges: Secure Subsystems
Secure card-embedded peripherals / subsystems
  e.g. modules, displays, keyboards, sensors
  secure packaging
Tamper-resistant integration
  secure interconnection
Secured interfacing
  security of internal bus for the various elements
  security of contact or contactless communication

## Slide 42: Challenges: Secure OS / Software
Operating Systems with increased security
  secure multi-application OS
  secure software updates or loading of applets
Development tools
  must be tailored to enhanced security concepts
Secure implementation of advanced crypto algorithms
Develop evaluation methods for security
  (e. g. modify CC methodologies for re-configurable architecture)

## Slide 43: Challenges: Secure Communication
Smart card communication protocols secured with high-end cryptography
  high-performance and high-speed encryption and decryption processes
  secure interoperability
Secure smart cards integration in networks
  enhanced security of smart cards in the Internet environment
    end-to-end security
    “fault-tolerant” protocols (accidental vs. induced faults)

## Slide 44: Challenges: Secure Interaction with Card Accepting Devices (CADs)
Secure interconnection with ambient intelligent environments
Secure man-machine interface
Establish security and create trust for the CADs

## Slide 45: Challenges: Enhanced security for the overall smart card system
Mutual interplay of the various security features of the smart card system
  hardware-software co-design
  operating system/protocols
  applications/testability/evaluation
Security along the complete chain
  from semiconductor to card accepting device and background system
Interdisciplinary collaboration necessary